# Module 2 - Assignment

NOTE: all references to equations, figures, tables are from the text and not online materials

From An Introduction to Fire Dynamics:

8.1Given the following data on the ignition of cubes of activated charcoal, calculate by extrapolation the depth of a ‘semi-infinite slab’ (i.e. a layer) of this material that would be a spontaneous ignition risk at 40 (C.

| r0 (half side of cube) (mm) | Ta (crit) (K) |
| --- | --- |
| 25.40 | 408 |
| 18.60 | 418 |
| 16.00 | 426 |
| 12.50 | 432 |
| 9.53 | 441 |

From An Introduction to Combustion:

(Chapter 4)

4.5. Consider the overall oxidation reaction of Propane:

C3H8 + 5O2  3CO2 + 4H2O

The following global mechanism has been proposed for this reaction:

Reaction rate =

where CGS units (cm, s, gmol, kcal, K) are employed.

- Identify the order of the reaction with respect to propane.

- Identify the order of reaction with respect to O2.

- What is the overall order of the global reaction?

- Identify the activation energy of the reaction.

4.11 Plot the forward rate constant for the reaction O + N2  NO + N versus temperature for the temperature range 1500 K < T < 2500 K. The rate constant is given as  in units of cm3/gmol-s. What conclusions can you draw?